## Slide 1: Combinational Logic Functions
Multi-bit Signals and Functions
Most non-trivial digital logic functions have inputs/outputs with more than 2 values
  BCD in/out; need 4 bits per each digit
Therefore a multi-bit output function is really composed of many single-bit functions, each a function of all input bits
  F (A) = (F3, F2, F1, F0) where each Fi is
  Fi = f(A3, A2, A1, A0)
A multi-bit signal is known as a VECTOR
Output is function of input only
  i.e. no feedback

## Slide 2: Combinational Circuits
Output is function of input only
  i.e. no feedback
  When input changes, output may change (after a delay)
•
•
•
•
•
•
n inputs
m outputs
Combinational
Circuits


## Slide 3: Vector Components and Functions
The single-bit components of a vector are usually assigned the vector name with index
  Index can be ordered left-to-right or right-to-left
  Numbered 0 to n-1 or 1 to n
Vector functions can be defined as unary constants, transfers, inversion
Binary vector functions defined on associated single-bit inputs (scalers)
  Generally classified as logical, shift, arithmetic

## Slide 4
Enabling
Enable signals permit or prevent something from occuring (a control signal)
  State is described as either:
    Active - ON or Enabled
    Passive - OFF or Disabled
  Polarity of control state can be:
    Active high - schematic symbol doesn’t have bubble
    Active low - Schematic symbol has bubble
A single enable signal may control vector operations (e.g. multi-bit 3-state buffer)

## Slide 5: Decoders
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number
A decoder is nothing more than a minterm generator with enable
A decoder generates appropriate minterms based on control signals
Binary Decoder
x1
x0
Only one lamp will turn on
0
0
1
0
0
0
1
0
2
3

## Slide 6: Decoders
2-to-4 Line Decoder
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 0 0 0 1
0 1 | 0 0 1 0
1 0 | 0 1 0 0
1 1 | 1 0 0 0
Binary Decoder
I1
I0
y3
y2
y1
y0

## Slide 7: Decoders
3-to-8 Line Decoder
Binary Decoder
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0

## Slide 8: Decoders
“Enable” Control
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
E | I1 I0 | Y3 Y2 Y1 Y0
0 | x x | 0 0 0 0
1 | 0 0 | 0 0 0 1
1 | 0 1 | 0 0 1 0
1 | 1 0 | 0 1 0 0
1 | 1 1 | 1 0 0 0

## Slide 9: Decoders
Expansion
I2 I1 I0 | Y7 Y6 Y5 Y4 Y3 Y2 Y1 Y0
0 0 0 | 0 0 0 0 0 0 0 1
0 0 1 | 0 0 0 0 0 0 1 0
0 1 0 | 0 0 0 0 0 1 0 0
0 1 1 | 0 0 0 0 1 0 0 0
1 0 0 | 0 0 0 1 0 0 0 0
1 0 1 | 0 0 1 0 0 0 0 0
1 1 0 | 0 1 0 0 0 0 0 0
1 1 1 | 1 0 0 0 0 0 0 0
I2 I1 I0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0
Y7
Y6
Y5
Y4
Y3
Y2
Y1
Y0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0

## Slide 10: Decoders
Active-High / Active-Low
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 0 0 0 1
0 1 | 0 0 1 0
1 0 | 0 1 0 0
1 1 | 1 0 0 0
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 1 1 1 0
0 1 | 1 1 0 1
1 0 | 1 0 1 1
1 1 | 0 1 1 1
Binary Decoder
I1
I0
Y3
Y2
Y1
Y0
Binary Decoder
I1
I0
Y3
Y2
Y1
Y0

## Slide 11: Implementation Using Decoders
Each output is a minterm
All minterms are produced
Sum the required minterms
Example: Full Adder
S(x, y, z) = ∑(1, 2, 4, 7)
C(x, y, z) = ∑(3, 5, 6, 7)
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Decoder
x
y
z
S C

## Slide 12: Implementation Using Decoders
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Decoder
x
y
z
S C
I2
I1
I0
Y7
Y6
Y5
Y4
Y3
Y2
Y1
Y0
Binary Decoder
x
y
z
S C

## Slide 13: Encoders
Put “Information” into code
Binary Encoder
  Example: 4-to-2 Binary Encoder
x3 x2 x1 | y1 y0
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 1 0
1 0 0 | 1 1
1
2
3
Binary Encoder
y1
y0
x1
x2
x3
Only one switch should be activated at a time

## Slide 14: Encoders
Octal-to-Binary Encoder (8-to-3)
I7 I6 I5 I4 I3 I2 I1 I0 | Y2 Y1 Y0
0 0 0 0 0 0 0 1 | 0 0 0
0 0 0 0 0 0 1 0 | 0 0 1
0 0 0 0 0 1 0 0 | 0 1 0
0 0 0 0 1 0 0 0 | 0 1 1
0 0 0 1 0 0 0 0 | 1 0 0
0 0 1 0 0 0 0 0 | 1 0 1
0 1 0 0 0 0 0 0 | 1 1 0
1 0 0 0 0 0 0 0 | 1 1 1
Binary Encoder
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0

## Slide 15: Priority Encoders
4-Input Priority Encoder
I3 I2 I1 I0 | Y1 Y0 | V
0 0 0 0 | 0 0 | 0
0 0 0 1 | 0 0 | 1
0 0 1 x | 0 1 | 1
0 1 x x | 1 0 | 1
1 x x x | 1 1 | 1
Priority Encoder
V
Y1
Y0
I3
I2
I1
I0
Y1 |  |  |  | I1 |  |  | 
 |  | 1 | 1 | 1 | 1 | I2 | 
I3 |  | 1 | 1 | 1 | 1 |  | 
 |  | 1 | 1 | 1 | 1 |  | 
 |  |  | I0 |  |  |  | 

## Slide 16: Encoder / Decoder Pairs
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Encoder
Binary Decoder
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 17: Multiplexers
2-to-1 MUX
4-to-1 MUX
MUX
Y
I0
I1
S
MUX
Y
I0
I1
I2
I3
S1 S0

## Slide 18: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
x y | F
0 0 | 1
0 1 | 1
1 0 | 0
1 1 | 1
Example F(x, y) = ∑(0, 1, 3)
x y
F
1
1
0
1

## Slide 19: Implementation Using Multiplexers
x y z | F
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 0
1 0 1 | 0
1 1 0 | 1
1 1 1 | 1
Example F(x, y, z) = ∑(1, 2, 6, 7)
MUX
Y
I0
I1
I2
I3 I4
I5
I6
I7
S2 S1 S0
x y z
0
1
1
0
0
0
1
1
F

## Slide 20: Multiplexer / DeMultiplexer Pairs
Y
I7
I6
I5
I4 I3
I2
I1
I0
I
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
MUX
DeMUX
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
S2 S1 S0
S2 S1 S0
x2 x1 x0
y2 y1 y0
Synchronize